Thomas Marangoni 01634007
16 March 2021
Bachelor Thesis
TU Wien, Automation Systems Group
Device and Link Discovery in Industrial Ethernet Networks

---
Industry 4.0
Interoperability
Automation
Flexibility
Open- and vendor- independent protocols
(eg. Time-Sensitive Networking (TSN))
Modular systems with high reconfigurability and reusability
Detection of the network configuration and
reconfiguration with a single button press

---
LLDP
Link Layer Discovery Protocol
Open and vendor-independent protocol
Advertisement of identity and capabilities
Daemon is broadcasting information
Daemon is collecting information from neighbors
One-Way protocol => No Acknowledgments

---
SNMP
Simple Network Management Protocol
Open and vendor-independent protocol
Network monitoring and management
Three different Versions
Connectionless Protocol based on UDP
Possibility of Notifications via Traps
Uses MIB for data

---
NETCONF
Network Configuration Protocol
Open and vendor-independent protocol
Network monitoring and management
Uses Remote Procedure Calls (RPC)
Session Based Protocol
Possibility of Notifications
Uses YANG for data

---
Better Routes
with more Information for TSN
Network graphs with ports
Link speed
Link length
Link material

---
Network Scanning Flow
Network devices are using LLDP & SNMP
Nodes have SNMP traps installed
Parallel SNMP detection scan
Full SNMP scan per device
Network Graph gets rebuilt after every scan

---
Requirements
For devices - Part I
SNMP daemon
Support SNMPv1 and SNMPv2c
LLDP daemon
LLDP MIB Entry
Each port needs to have a unique MAC address

---
Requirements
For devices - Part II
LLDPd must send the port MAC address as ChassisID
Remote port data must be connected to a local port in the MIB data
Every network node (except end nodes) must send an SNMPv1 trap to the application on interface change

---
Firmware
Material of link
Different MIB data between firmware versions on the same model.
There is no standardized way to access the material of a link.
OID Alias
Non existing MAC-Address
Every manufacture can have a own OID table, which represents the same data defined in standardized OID tables.
Some devices are returning MAC-Addresses for ports on LLDP, which don’t exist in any interface entry.
Length of link
LLDP connected to Bridge
There is no default way to get the length of a link between two device.
Some manufactures are linking the collected LLDP data to the whole bridge and not single ports.

---
Results
Contribution and Conclusion
Partly working prototype
SNMP has its limits, NETCONF would be better
Work from manufacturer needed
Thesis on GitHub.com/ThomasMarangoni/discovery

---
Thank you!
Slide design from LibreOffice
Thesis on GitHub
ThomasMarangoni/discovery